## Slide 1: Chapter 2
Image Processing Basics

## Slide 2: What will we learn?
How is a digital image represented and stored in memory?
What are the main types of digital image representation?
What are the most popular image file formats?
What are the most common types of image processing operations and how do they affect pixel values?

## Slide 3: Digital Image Representation

## Slide 4: Raster vs Vector
Raster (or bitmap) image format = one or more 2D arrays of pixels
– Good quality and fast display speed but larger memory storage requirement and size dependency
Vector image format = series of drawing commands
– Resizing without introducing artifact, less size but need to be rasterized for display divices

## Slide 5: Example
A binary image and the pixel values in a 6×6 neighborhood
In Matlab it is called logical array of 0's and 1's

## Slide 6: A gray-level image and the pixel values in a 6×6 neighborhood
Gray-level, monochrome, grayscale In Matlab most popular are uint8 ( 0=black, 255=white), uint16 (0=black, 65535=white), double (0.0=black, 1.0=white)

## Slide 7: Color Images
RGB, a 24-bit number 8bits for each of RED, GREEN and BLUE
Indexed representation. A pixel contains an index to the pallete of colors...

## Slide 8: Color Image, R, G and B

## Slide 9: Indexed Image...

## Slide 10: Some Image File Formats
Lossy vs Lossless Compression
  BIN, PPM (PBM,PGM, PNM) – raw pixel data
Need to know all sizes, bytes per pixel etc
  BMP – Microsoft Windows
  JPEG – most popular for photographic quality images
  GIF – uses indexed representation of colors with maximum of 256 colors palette
  TIFF – 24bit per pixel (truecolor), 5 different compression schemes
  PNG – supports both indexed and truecolor format, patent free replacement for GIF
  RAW – adopted by camera manufacturers

## Slide 11: Basic Terminology
Image Topology. It involves the investigation of fundamental image properties, such as number of a particular object, number of separate (not connected) regions, and number of holes in an object etc.
Neighborhood. The pixels surrounding a given pixel constitute its neighborhood, which can be interpreted as a smaller matrix containing (and usually centered around) the reference pixel.

## Slide 12: (a) 4-neighborhood, (b) diagonal neighborhood, (c) 8-neighborhood

## Slide 13: Basic Terminology (cont.)
Adjacency: 2 pixel p and q are 4-adjacent if they are 4-neighbors of each other
8-adjacency – similar.
Paths. A 4-path between two pixels p and q is a sequence of pixels starting with p and ending with q such that each pixel in the sequence is 4-adjacent to its predecessor in the sequence.
8-path – similar.

## Slide 14: Basic Terminology (cont.)
Connectivity. If there is a 4-path between pixels p and q, they are said to be 4-connected
8-connected
Components. A set of pixels that are connected to each other is called a component. (a) original (binary) image (b) results for 8-connectivity (c) results for 4-connectivity.

## Slide 15: Basic Terminology (cont.)
Distances Between Pixels

## Slide 16: Image Processing Operations
Operations in the Spatial Domain
  Global (Point) Operations
  Neighborhood-Oriented Operations
  Operations Combining Multiple Images
Operations in a Transform Domain
  Fourier Transform
  Discrete Cosine Transform

## Slide 17: Intensity reduction by 2 (global operation)

## Slide 18: Combining Two Images

## Slide 19: Sharpening an image by neighborhood operation

## Slide 20: Operations in Transform Domain

## Slide 21: References
Practical Image and Video Processing using Matlab, Oge Marques, 2011, Chapter 2